## Slide 1: COMPUTER NETWORKS
THE DATALINK LAYER

## Slide 2: Chapter 3: Data Link layer
our goals:
understand principles behind link layer services:
  framing
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing (MAC address)
  local area networks: Ethernet, VLANs
instantiation, implementation of various link layer technologies

## Slide 3: Link layer, LANs: outline
6.1 introduction, services
6.2 framing
6.3 error detection, correction
6.4 data link protocols
- stop-n-wait
- stop-n-wait ARQ
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Presentation
Session
Transport
Network
Data Link
Physical
10010111001011010010110101011110101
segments
packets
frames
Data
Data
Data
Data

## Slide 4: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 5: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide rdt over link
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourists = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 6: Link layer services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, destination
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this in chapter 3
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 7: Link layer services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  For half-duplex, nodes at both ends of link can transmit, but not at same time
  Full-duplex: both nodes can send at the same time

## Slide 8: Where is the link layer implemented?
In each and every host, link layer implemented in “adaptor” (aka adapter, network interface card-NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 9: Adaptors communicating
Sending side
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
Receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 10: Link layer, LANs: outline
6.1 introduction, services
6.2 framing
6.3 error detection, correction
6.4 elementary data link protocols
- stop-n-wait
- stop-n-wait ARQ

## Slide 11: Framing Methods
Byte count.
Flag bytes with byte stuffing.
Flag bytes with bit stuffing.
Physical layer coding violations.

## Slide 12: Framing Methods
Frame Header − It contains the source and the destination addresses of the frame.
Payload field − It contains the message to be delivered.
Trailer − It contains the error detection and error correction bits.
Flags − 1- byte (8-bits) flag at the beginning and at end of the frame. It is a protocol – dependent special character, signalling the start and end of the frame.

## Slide 13: Framing (1): Byte count
A byte stream. (a) Without errors. (b) With one error.
Sending
Receiving

## Slide 14: Framing (2): Flag with byte stuff
A frame delimited (split) by flag bytes.
In byte stuffing, a special byte called the escape character (ESC) is stuffed before every byte in the message with the same pattern as the flag byte. If the ESC sequence is found in the message byte, then another ESC byte is stuffed before it.
https://www.tutorialspoint.com/what-is-byte-stuffing-in-computer-networks
ç
Prevent duplicate special bytes in payload message

## Slide 15: Framing (2): Flag with byte stuff
A frame delimited (split) by flag bytes.
Four examples of byte sequences before and after byte stuffing.
10101010
10101010
https://www.tutorialspoint.com/what-is-byte-stuffing-in-computer-networks

## Slide 16: Framing (3): Flag with bit stuff
Bit stuffing. (a) The original data. (b) The data as they appear on
the line. (c) The data as they are stored in the receiver’s memory after destuffing.
Whenever a 0 bit is followed by five consecutive 1bits in the message, an extra 0 bit is stuffed at the end of the five 1s. When the receiver receives the message, it removes the stuffed 0s after each sequence of five 1s.
https://www.tutorialspoint.com/what-is-bit-stuffing-in-computer-networks
Prevent duplicate flag bit pattern in payload message

## Slide 17: Framing (4): Physical layer coding violations
This method is only applicable to networks in which the encoding on the physical medium contains some redundancy.
  For example, some LANs encode 1 bit of data by using 2 physical bits. Normally, a 1 bit is a high-low pair and a 0 bit is a low-high pair.
11 or 00 are not used for data but are used for delimiting (splitting) frames in some protocols.

## Slide 18: Exercise
Computer networks, Chapter 3, p.252
  Exercise 2
  Exercise 6

## Slide 19: Link layer, LANs: outline
6.1 introduction, services
6.2 framing
6.3 error detection, correction
6.4 elementary data link protocols

## Slide 20: Error detection
EDC: Error Detection and Correction bits (redundancy)
D : Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
otherwise

## Slide 21: Error detection
Parity check
Internet checksum
Cyclic redundancy check (CRC)

## Slide 22: Parity checking
Single bit parity:
detect single bit errors
Two-dimensional bit parity:
detect and correct single bit errors
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
  The two types of parity checking are
    Even Parity
    Odd Parity
https://www.tutorialspoint.com/what-is-a-parity-bit
Number of 1s bits is even -> parity bit is 0
Number of 1s bits odd -> parity bit is 1

## Slide 23: Internet checksum (1)
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?
Goal: detect “errors” (i.e., flipped bits) in transmitted packet (Note: used at transport layer only)

## Slide 24: Internet checksum (2)
Transmitter
Receiver
Step1: Now, all the segments are added and the result is obtained as:
10011001 + 11100010 + 00100100 + 10000100 = 1000100011
Step 2: Since the result consists of 10 bits, so extra 2 bits are wrapped around.
00100011 + 10 = 00100101 (8 bits)
Step3: 1’s complement is taken which is 11011010.
Thus, Checksum value = 11011010
Transmit Data + Checksum
Sum of all segments (wrapped around) + Checksum value
= 00100101 + 11011010 = 11111111
No errors

## Slide 25: Exercise
Computer networks, Chapter 3, p. 253
  Exercise 15

## Slide 26: Cyclic redundancy check (CRC)
more powerful error-detection coding
view data bits, D, as a binary number
Let r be the degree of (generator), G
  e.g. G(x) = x3 + 1 = 1.x3 + 0.x2 + 0.x1 + 1.x0 => G = 1001, r = 3
Goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)

## Slide 27: CRC example
want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R to satisfy:
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
r bits
1 0 1 1 1 0 0 1 1
Transmit
)

## Slide 28: CRC example
0 0 0 0
At the receiver
1 0 1 1 1 0 0 1 1
Receive
1 0 0 1
G
1 0 0 1
1 0 1
1 0 1 0 1 1
0 0 0
1 0 1 0
1 0 0 1
1 1 0
0 0 0
1 1 0 1
1 0 0 1
1 0 0 1
1 0 0 1

## Slide 29: Elementary Data Link Protocols (2)
Implementation of the physical, data link, and network layers.

## Slide 30: Exercise
Computer Networks, Chapter 3, p. 253
  Exercise 16, 17

## Slide 31: Link layer, LANs: outline
6.1 introduction, services
6.2 framing
6.3 error detection, correction
6.4 elementary data link protocols

## Slide 32: Elementary Data Link Protocols (1)
Utopian Simplex Protocol
Simplex Stop-and-Wait Protocol
  Error-Free Channel
Simplex Stop-and-Wait Protocol
  Noisy Channel
Sliding Window Protocol
  Go-back-N
  Selective repeat

## Slide 33: Utopian Simplex Protocol (1)
It is hypothetical protocol designed for unidirectional data transmission over an ideal channel, i.e. a channel through which transmission can never go wrong. Since this protocol is totally unrealistic, it is often called Utopian Simplex protocol.
Example Utopian protocol written in C

## Slide 34: Simplex Stop-and-Wait Protocol for a Noisy Channel (1)
Simplex Stop – and – Wait protocol for noisy channel is data link layer protocol for data communications with error control and flow control mechanisms.
It is popularly known as Stop – and –Wait Automatic Repeat Request (Stop – and – Wait ARQ) protocol. It adds error control facilities to Stop – and – Wait protocol.

## Slide 35: Simplex Stop-and-Wait Protocol for a Noisy Channel (2)
Example Stop and Wait protocol written in C

## Slide 36: Sliding Window Protocols (1)
In this protocol, multiple frames can be sent by a sender at a time before receiving an acknowledgment from the receiver. The term sliding window refers to the imaginary boxes to hold frames.
the sender has a buffer called the sending window and the receiver has buffer called the receiving window.
two categories
  Go – Back – N ARQ
  Selective Repeat ARQ

## Slide 37: Protocol Using Go-Back-N (1)
Pipelining and error recovery. Effect of an error when
(a) receiver’s window size is 1

## Slide 38: Protocol Using Go-Back-N (2)
Pipelining and error recovery. Effect of an error when
(b) receiver’s window size is large.

## Slide 39: Protocol Using Selective Repeat (1)
This protocol also provides for sending multiple frames before receiving the acknowledgment for the first frame. However, here only the erroneous or lost frames are retransmitted, while the good frames are received and buffered.

## Slide 40: Example Data Link Protocols
HDLC – High-Level Data Link Control
The Data Link Layer in the Internet

## Slide 41: HDLC – High-Level Data Link Control
HDLC is a group of data link (Layer 2) protocols used to transmit synchronous data packets between point-to-point nodes (RFC 1662).
HDLC uses a zero-insertion/deletion process (bit stuffing) to ensure that the bit pattern of the delimiter flag does not occur in the fields between flags.

## Slide 42: HDLC – High-Level Data Link Control
Frame format for bit-oriented protocols.
Data is usually sent in multiples of 8 bits, but only some variants require this; others theoretically permit data alignments on other than 8-bit boundaries.
The frame check sequence (FCS) is a 16-bit CRC or a 32-bit CRC computed over the Address, Control, and Information fields.

## Slide 43: HDLC – High-Level Data Link Control
Control field:
(a) An information frame.
(b) A supervisory frame.
(c) An unnumbered frame.
https://www.tutorialspoint.com/high-level-data-link-control-hdlc

## Slide 44: Practice
Packet Tracer
  Generate a HDLC between 2 router A and B over a serial link.
Serial link
Clock: 2500000 Hz
192.168.10.1/30
192.168.10.2/30
192.168.1.2/24
192.168.1.1/24
192.168.2.1/24
192.168.2.2/24
Router-B(config)#interface serial 0/0/0
Router-B(config-if)#clock rate 250000
//////////////////////////
Router-B(config)#interface serial 0/0/0
Router-B(config-if)#encapsulation hdlc
Router-B(config-if)#ip address 192.168.10.2 255.255.255.252
Router-B(config-if)#no shutdown
//////////////////////////
Router-A(config)#interface serial 0/0/0
Router-A(config-if)#encapsulation hdlc
Router-A(config-if)#ip address 192.168.10.1 255.255.255.252
Router-A(config-if)#no shutdown
Router-B#ping 192.168.10.1
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 192.168.10.5, timeout is 2 seconds:
!!!!! Success rate is 100 percent (5/5), round-trip min/avg/max = 3/3/4 ms

## Slide 45: Summary
Principles of data link layer services:
  Framing
    Byte count.
    Flag bytes with byte stuffing.
    Flag bytes with bit stuffing.
  Error detection and correction
    Parity check
    Internet checksum
    CRC
  Elementary data link protocols
    Utopian Simplex Protocol
    Simplex Stop-and-Wait Protocol
      Noisy Channel
    Sliding window Protocol
      Go-back-N
      Selective Repeat

## Slide 46
Appendix (not in exams)

## Slide 47: Utopian Simplex Protocol (2)
A utopian simplex protocol.
. . .

## Slide 48: Utopian Simplex Protocol (3)
A utopian simplex protocol.
Go back to Utopian protocol

## Slide 49: Elementary Data Link Protocols (3)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h.
. . .

## Slide 50: Elementary Data Link Protocols (4)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h.
. . .

## Slide 51: Elementary Data Link Protocols (5)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h.

## Slide 52: Simplex Stop-and-Wait Protocol for a Noisy Channel (3)
A simplex stop-and-wait protocol.
. . .

## Slide 53: Simplex Stop-and-Wait Protocol for a Noisy Channel (4)
A simplex Stop-and-Wait protocol.
Go back to Stop and Wait protocol

## Slide 54: Sliding Window Protocols (2)
A positive acknowledgement with retransmission protocol.
. . .

## Slide 55: Sliding Window Protocols (2)
A positive acknowledgement with retransmission protocol.
. . .

## Slide 56: Sliding Window Protocols (4)
A positive acknowledgement with retransmission protocol.

## Slide 57: Sliding Window Protocols (5)
A sliding window of size 1, with a 3-bit sequence number. (a) Initially. (b) After the first frame has been sent.

## Slide 58: Sliding Window Protocols (6)
A sliding window of size 1, with a 3-bit sequence number
(c) After the first frame has been received. (d) After the first acknowledgement has been received.

## Slide 59: One-Bit Sliding Window Protocol (1)
A 1-bit sliding window protocol.
. . .

## Slide 60: One-Bit Sliding Window Protocol (2)
A 1-bit sliding window protocol.
. . .

## Slide 61: One-Bit Sliding Window Protocol (3)
A 1-bit sliding window protocol.

## Slide 62: One-Bit Sliding Window Protocol (4)
Two scenarios for protocol 4. (a) Normal case. (b) Abnormal
case. The notation is (seq, ack, packet number). An asterisk indicates where a network layer accepts a packet

## Slide 63: Protocol Using Go-Back-N (3)
A sliding window protocol using go-back-n.
. . .

## Slide 64: Protocol Using Go-Back-N (4)
A sliding window protocol using go-back-n.
. . .

## Slide 65: Protocol Using Go-Back-N (5)
A sliding window protocol using go-back-n.
. . .

## Slide 66: Protocol Using Go-Back-N (6)
A sliding window protocol using go-back-n.
. . .

## Slide 67: Protocol Using Go-Back-N (7)
A sliding window protocol using go-back-n.
. . .

## Slide 68: Protocol Using Go-Back-N (8)
A sliding window protocol using go-back-n.
. . .

## Slide 69: Protocol Using Go-Back-N (9)
A sliding window protocol using go-back-n.

## Slide 70: Protocol Using Go-Back-N (10)
Simulation of multiple timers in software. (a) The queued timeouts (b) The situation after the first timeout has expired.

## Slide 71: Protocol Using Selective Repeat (2)
A sliding window protocol using selective repeat.
. . .

## Slide 72: Protocol Using Selective Repeat (3)
A sliding window protocol using selective repeat.
. . .

## Slide 73: Protocol Using Selective Repeat (4)
A sliding window protocol using selective repeat.
. . .

## Slide 74: Protocol Using Selective Repeat (5)
A sliding window protocol using selective repeat.
. . .

## Slide 75: Protocol Using Selective Repeat (6)
A sliding window protocol using selective repeat.
. . .

## Slide 76: Protocol Using Selective Repeat (7)
A sliding window protocol using selective repeat.
. . .

## Slide 77: Protocol Using Selective Repeat (7)
A sliding window protocol using selective repeat.
. . .

## Slide 78: Protocol Using Selective Repeat (8)
A sliding window protocol using selective repeat.
. . .

## Slide 79: Protocol Using Selective Repeat (9)
A sliding window protocol using selective repeat.

## Slide 80: Protocol Using Selective Repeat (10)
Initial situation with a window of size 7
After 7 frames sent and received but not acknowledged.
Initial situation with a window size of 4.
After 4 frames sent and received but not acknowledged.