## Slide 1: Medium Access Control (MAC) LAYER
COMPUTER NETWORKS

## Slide 2: Chapter 4: outline
4.1 Allocation problem for a broadcast channel
- Multiple access problem
4.2. Control access protocols
  ALOHA
  Slotted ALOHA
  CSMA (CA/CD)
  Collision-free
4.3. LAN technologies
  LAN MAC Address &ARP
  Ethernet
  Wi-Fi 802.11
  WiMax 802.16
  Bluetooth
  4G LTE
  RFID

## Slide 3: Multiple access links, protocols
two types of “links”:
Point-to-point (discussed in Chapter 2&3)
  PPP for dial-up access
  point-to-point link between Ethernet switch, host
Broadcast (shared wire or shared medium)
  old-fashioned Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 4: Multiple access protocols
Single shared broadcast channel
Two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
Multiple Access Protocol
Distributed algorithm that determines how nodes share channel,
  When nodes can transmit
Communication about channel sharing must use channel itself!
  No out-of-band channel for coordination

## Slide 5: An ideal multiple access protocol
Given: broadcast channel of rate R bps
Desired rate:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. Fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. Simple

## Slide 6: MAC protocols: taxonomy
Three broad classes:
channel partitioning
  divide channel into smaller “pieces”
    time slots, frequency, code
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 7: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 8: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 9: Chapter 4: outline
4.1 Allocation problem for a broadcast channel
- Multiple access problem
4.2. Control access protocols
  ALOHA
  Slotted ALOHA
  CSMA (CD/CA)
  Collision-free
4.3. LAN technologies
  LAN MAC Address & ARP
  Ethernet
  Wi-Fi 802.11
  WiMax 802.16
  Bluetooth
  4G
  IoT
  RFID

## Slide 10: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes at the same time ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  ALOHA
  slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 11: Pure (unslotted) ALOHA
Unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 12: Slotted ALOHA
Assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only at the beginning of slot
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
Operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with probability p until success

## Slide 13: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 14: CSMA (carrier sense multiple access)
CSMA: listen before transmit:
if channel sensed idle: transmit entire frame
if channel sensed busy, defer transmission
human analogy: don’t interrupt others!

## Slide 15: CSMA collisions
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 16: CSMA/CD (collision detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
Collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
Human analogy: the polite conversationalist
https://www.geeksforgeeks.org/collision-detection-csmacd/

## Slide 17: CSMA/CD (collision detection)
spatial layout of nodes

## Slide 18
Time
MS A’s frame
MSs B & C sense the medium
MS B resenses the medium and transmits its frame
MS B’s frame
Backoff -delay for B
Backoff - delay for C
MS C resenses the medium but defers to MS B
CSMA/CA (CSMA with Collision Avoidance)
A basic collision avoidance (CA) scheme
CSMA/CA rule: Backoff before collision (to avoid collisions)
(Modified by LTL)

## Slide 19
When medium idle for a period ≥ DIFS => can transmit immediately
  DIFS = Distributed InterFrame Space
    In 802.11b networks, DIFS = 50 μs
© 2006, Michael Hall, Helsinki Univ. of Technology
DIFS
->
(Modified by LTL)
CSMA/CA (CSMA with Collision Avoidance)

## Slide 20: “Taking turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 21: “Taking turns” MAC protocols
polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 22: “Taking turns” MAC protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T

## Slide 23
cable headend
CMTS
ISP
cable modem
termination system
multiple 40Mbps downstream (broadcast) channels
  single CMTS transmits into channels
multiple 30 Mbps upstream channels
  multiple access: all users compete certain upstream channel time slots (others assigned)
Cable access network
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
upstream Internet frames, TV control, transmitted
upstream at different frequencies in time slots

## Slide 24
DOCSIS: data over cable service interface spec
FDM over upstream, downstream frequency channels
TDM upstream: some slots assigned, some have contention
  downstream MAP frame: assigns upstream slots
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots
MAP frame for
Interval [t1, t2]
Residences with cable modems
Downstream channel i
Upstream channel j
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS
Cable access network

## Slide 25: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring

## Slide 26: Exercise
Compare CSMA/CD vs CSMA/CA ?

## Slide 27: Chapter 4: outline
4.1 Allocation problem for a broadcast channel
- Multiple access problem
4.2. Control access protocols
  ALOHA
  Slotted ALOHA
  CSMA (CD/CA)
  Collision-free
4.3. LAN technologies
  LAN MAC Address & ARP
  Ethernet
  Wi-Fi 802.11
  WiMax 802.16
  Bluetooth
  4G
  IoT
  RFID

## Slide 28: MAC addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 29: MAC addresses and ARP
each adapter on LAN has unique MAC address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 30: MAC addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached

## Slide 31: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 32: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 33: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 34: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 35: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 36: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 37: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 38: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 39: Chapter 4: outline
4.1 Allocation problem for a broadcast channel
- Multiple access problem
4.2. Control access protocols
  ALOHA
  Slotted ALOHA
  CSMA (CD/CA)
  Collision-free
4.3. LAN technologies
  LAN MAC Address & ARP
  Ethernet 802.3
  Wi-Fi 802.11
  WiMax 802.16
  Bluetooth
  4G
  IoT
  RFID

## Slide 40: Ethernet
“dominant” wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch

## Slide 41: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain
  can collide with each other
star: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol
    nodes do not collide with each other
switch
bus: coaxial cable
star

## Slide 42: Ethernet frame structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 43: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 44: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 45: 802.3 Ethernet standards: link & physical layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer

## Slide 46: Ethernet (IEEE 802.3)
Classic Ethernet
  Shared medium
  2.5 km max + 4 repeaters
Switched Ethernet
  Fast Ethernet : 100 Mbps
  Gigabit Ethernet
  10 Gigabit Ethernet
Thick Ethernet : 500 m, 100 users
Thin Ethernet: 185 m, 30 users

## Slide 47: Ethernet: CSMA/CD with Binary Exponential Backoff
After i’th consecutive collision, the sender nodes wait a random number of time slots between 0 and 2^i − 1.
Each Time slot = 51.2 μsec = 512 bit times
after 10 collisions, the interval is frozen at maximum 1023 slots.
After 16 collisions, the controller reports failure back

## Slide 48: Efficiency of Ethernet at 10 Mbps with 512-bit slot times

## Slide 49: Switched Ethernet (1)
(a) Hub. (b) Switch.

## Slide 50: Switched Ethernet (2)
An Ethernet switch.
Switch
Twisted pair
Switch ports
Hub

## Slide 51: Fast Ethernet
100B-T4: uses 4 twisted pairs with 25 MHz BW. 1 to the switch, 1 from the switch and other 2 are interchangeable. Using 3 voltage levels for symbols. Manchester encoding.
100B-TX: 4B/5B encoding. 125 MHz BW results 100 Mbps. 2 pairs of cable required.
100B-FX: only works with switches because the maximum cable length should be less than 250 m for CD to work.

## Slide 52: Gigabit Ethernet
Two ways to enhance cable length to 200 m when using hubs:
  Hardware carrier extension to 512 bytes.
  frame bursting
8B/10B encoding is used to maintain synchronization.
In UTP cables all 4 pairs are used in simultaneous full-duplex mode! With 5 voltage levels
Pause frames are defined to cease the communication speed.

## Slide 53: 10 Gigabit Ethernet
Fiber cables use 64B/66B coding is used.
CX cables use 8B/10B coding and 3.125 Gsymbol/sec on each pair.
T cabling requires 16 voltage levels. LDPC (Low Density Parity Check) is used.
40Gbps and 100Gbps Ethernet standards are in the way.

## Slide 54: Ethernet benefits
Reliable: by introducing switches
Cheap: twisted pairs and NICs
Easy to maintain: no software requirement. Easy configuration.
Well integration with IP: both are connection less.
Flexible: evolve by time in speed requirements with minimum reconfiguration and changes.

## Slide 55: Wireless LAN 802.11
802.11 architecture and protocol stack
802.11 physical layer
802.11 MAC sublayer protocol
802.11 frame structure
Services

## Slide 56: 802.11 Architecture and Protocol Stack (1)
802.11 architecture – infrastructure mode
Access Point
Client
To Network

## Slide 57: 802.11 Architecture and Protocol Stack (2)
802.11 architecture – ad-hoc mode-

## Slide 58: 802.11 Protocol Stack
1-2 Mbps 11 Mbps 54 Mbps 600 Mbps

## Slide 59: 802.11b PHY Layer
1 Mbps : 11 chip barker code to spread the signal with BPSK to send 1 bit per 11 chip. The chip rate is 11 Mchips/sec.
2 Mbps : QPSK to send 2 bits per 11 chip.
5.5 Mbps: CCK (Complementary Code Keying) with 4 bits per 8 chips.
11 Mbps: CCK with 8 bits per 8 chips.

## Slide 60: 802.11a, g, n PHY Layer
802.11a Works in 5GHz band.
Uses OFDM with 52 subcarriers 48 for data and 4 for sync.
Each symbol lasts 4μs and sends 1, 2, 4, or 6 bits.
Supports 8 data rates from 6 up to 54Mbps.
Communication range is 1/7 802.11b because of freq. band.
802.11 g uses OFDM in 2.4GHz band.
Supports same rates of 802.11a with same range of 802.11b
802.11n doubles the channel width from 20 to 40MHz.
Uses multiple antennas and MIMO techniques to increase BW.

## Slide 61: The 802.11 MAC Sublayer Protocol
Sending a frame with CSMA/CA.
The initial backoff gets exponentially bigger if no ack is received.

## Slide 62: Collision Avoidance mechanism
The use of virtual channel sensing using CSMA/CA.
NAV (Network Allocation Vector)
https://en.wikipedia.org/wiki/IEEE_802.11_RTS/CTS

## Slide 63: CSMA/CA
RTS/CTS mechanism is seldom used, because it slows down the communication.
The random back-off mechanism as well as virtual carrier sensing (by overhearing the NAV field) are the main mechanisms to avoid collision.
Fragmentation is also used to keep the frame error rates small.
Fragments are sent in bursts when channel is acquired and each fragment should be acknowledged before the next one is sent.

## Slide 64: Power management
Nodes go to sleep mode and inform AP of it.
AP buffers traffic for sleeping nodes.
AP sends periodic beacons to announce which node has a buffered frame.
Nodes should wake up at beacon intervals (typically 100msec) to see if they have frames.
If so they tell the AP to send them the frames.

## Slide 65: Interframe timing for QoS purposes
SIFS (Short InterFrame Spacing)
DIFS (Distributed Coordination Function InterFrame Spacing)
AIFS (Arbitration InterFrame Space)
EIFS (Extended InterFrame Spacing)

## Slide 66: 802.11 Frame Structure
Format of the 802.11 data frame

## Slide 67: Hub
Hub is the repeating device of the physical layer:
Bits coming from one link will come out any other links with the same speed
No buffer frame
No CSMA/CD at hub:
Provides network administration function
twisted pair
hub

## Slide 68: Connecting to hub
Backbone hub connects LAN segments
Extend maximum distance among nodes
But the segment's collision areas become larger
Unable to connect 10BaseT and 100BaseT
hub
hub
hub
hub

## Slide 69: Switch
The switch is the repeating device of the datalink layer
  Store and forward Ethernet frames
  Check the frame header and select frame for forwarding based on the MAC target address
  When the frame is forwarded on the segment, it uses CSMA/CD to access the segment
  Transparent: Hosts don’t know the existence of the switch
  plug-and-play: Switch does not require pre-configuration

## Slide 70: Forwarding
How to determine which frame to be forwarded to LAN segment? Similar to the routing problem...
hub
hub
hub
switch
1
2
3

## Slide 71: Ethernet switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 72: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 73: Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 74: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 75: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 76: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send
on just one link

## Slide 77: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram