## Slide 1: COMPUTER NETWORKS
THE NETWORK LAYER
Data Plane

## Slide 2
5.1 Overview of Network layer
  data plane
  control plane
5.2 What’s inside a router
5.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
5.4 routing protocols
link state
distance vector
5.5 intra-AS routing in the Internet: OSPF
5.6 routing among the ISPs: BGP
5.7 The SDN control plane
5.8 ICMP: The Internet Control Message Protocol
5.9 Network management and SNMP
Chapter 5: outline
Data Plane
Control Plane

## Slide 3: Network layer
transport segments from sending to receiving host
on sending side: encapsulates segments into datagrams
on receiving side: delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 4: Two key network-layer functions
Network-layer functions:
Forwarding: move packets from router’s input to appropriate router output
Routing: determine route taken by packets from source to destination
  routing algorithms
Analogy: taking a trip
forwarding: process of getting through single interchange
routing: process of planning trip from source to destination

## Slide 5: Network layer: data plane, control plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
1
2
3
0111
values in arriving
packet header

## Slide 6
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 7
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 8: Network service model
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
Q: What service model for “channel” transporting datagrams from sender to receiver?

## Slide 9: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 10
5.1 Overview of Network layer
  data plane
  control plane
5.2 What’s inside a router
5.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
  NAT
5.4 routing protocols
link state
distance vector
5.5 intra-AS routing in the Internet: OSPF
5.6 routing among the ISPs: BGP
5.7 The SDN control plane
5.8 ICMP: The Internet Control Message Protocol
5.9 Network management and SNMP
Chapter 4: outline
Data Plane
Control Plane

## Slide 11: Router architecture overview
high-level view of generic router architecture:
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operttes in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame

## Slide 12: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queueing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 4
switch
fabric

## Slide 13: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 4
switch
fabric

## Slide 14: Destination-based forwarding
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?
forwarding table

## Slide 15: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 16: Longest prefix matching
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: can up ~1M routing table entries in TCAM

## Slide 17: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 18: Switching via memory
First generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 19: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 20: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 21: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 22: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
This slide in HUGELY important!
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 23: Output port queueing
buffering when arrival rate via switch exceeds output line speed
  queueing (delay)
  loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 24: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) x link capacity C
  e.g., C = 10 Gpbs; link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N

## Slide 25: Scheduling mechanisms
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
  real-world example?
  discard policy: if packet arrives to full queue: who to discard?
    tail drop: drop arriving packet
    priority: drop/remove on priority basis
    random: drop/remove randomly
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)

## Slide 26: Scheduling policies: priority
Priority scheduling: send highest priority queued packet
multiple classes, with different priorities
  class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc.
  real world example?
high priority queue
(waiting area)
low priority queue
(waiting area)
arrivals
classify
departures
link
(server)
1
3
2
4
5
5
5
2
2
1
1
3
3
4
4
arrivals
departures
packet in service

## Slide 27: Scheduling policies: still more
Round Robin (RR) scheduling:
multiple classes
cyclically scan class queues, sending one complete packet from each class (if available)
real world example?
1
2
3
4
5
5
5
2
3
1
1
3
3
4
4
arrivals
departures
packet in service

## Slide 28: Scheduling policies: still more
Weighted Fair Queuing (WFQ):
generalized Round Robin
each class gets weighted amount of service in each cycle
real-world example?

## Slide 29
5.1 Overview of Network layer
  data plane
  control plane
5.2 What’s inside a router
5.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
  NAT
5.4 routing protocols
link state
distance vector
5.5 intra-AS routing in the Internet: OSPF
5.6 routing among the ISPs: BGP
5.7 The SDN control plane
5.8 ICMP: The Internet Control Message Protocol
5.9 Network management and SNMP
Chapter 5: outline
Data Plane
Control Plane

## Slide 30: The Internet network layer
host, router network layer functions:
forwarding
table
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 31: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 32: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 33: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1(MF)
length
=1500
ID
=x
offset
=185
fragflag
=1 (MF)
length
=1500
ID
=x
offset
=370
fragflag
=0 (DF)
length
=1060
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
(Since the scaling factor of the fragment offset is 8)
More fragments (MF = 1 bit) or Don’t fragment (DF = 1 bit)
Notes: Identification (16 bits) – use to identify fragments of the same frame.
Fragment offset (13 bits) – use to identify the sequence of fragments in the frame. It generally indicates a number of data bytes preceding or ahead of the fragment. Maximum fragment offset possible = (65535 – 20) = 65515 {where 65535 is the maximum size of datagram and 20 is the minimum size of IP header} So, we need ceil(log265515) = 16 bits for a fragment offset but the fragment offset field has only 13 bits. So, to represent efficiently we need to scale down the fragment offset field by 216/213 = 8 which acts as a scaling factor. Hence, all fragments except the last fragment should have data in multiples of 8 so that fragment offset ∈ N.
More fragments (MF = 1 bit) – tells if more fragments are ahead of this fragment i.e. if MF = 1, more fragments are ahead of this fragment and if MF = 0, it is the last fragment.
Don’t fragment (DF = 1 bit) – if we don’t want the packet to be fragmented then DF is set i.e. DF = 1.

## Slide 34
5.1 Overview of Network layer
  data plane
  control plane
5.2 What’s inside a router
5.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
  NAT
5.4 routing protocols
link state
distance vector
5.5 intra-AS routing in the Internet: OSPF
5.6 routing among the ISPs: BGP
5.7 The SDN control plane
5.8 ICMP: The Internet Control Message Protocol
5.9 Network management and SNMP
Chapter 5: outline
Data Plane
Control Plane

## Slide 35: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 36: IP addressing: introduction
Q: how are interfaces actually connected?
A: we’ll learnt about that in chapters 2-4.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station

## Slide 37: IP Address Classes

## Slide 38: Special IP addresses

## Slide 39: Net & Subnet
Routing operation inside a router:
  Routing prefix = (IP Address) AND (Net/Subnet mask)
  If Routing prefix (IP Source)  Routing prefix (IP Dest.) => route to another network.

## Slide 40: Subnet
Borrow 2 bit
  # of subnets = 22 = 4
  Subnet mask = 2 bits = 27 + 26 = 128 + 64 = 192 = 11000000
  Range of hosts (Number of IPs in subnet) = 26 = 64 = 01000000
S
S
H
H
H
H
H
H
 | Range | Binary | host IP range
 | 0 – 63 64 – 127 128 – 191 192 – 255 | 00 000000 – 00 111111 01 000000 – 01 111111 10 000000 – 10 111111 11 000000 – 11 111111 | 1 – 62 65 – 126 129 – 190 193 - 254

## Slide 41: Subnet
Borrow 3 bit
  # of subnets
  Subnet mask
  Range of hosts (Number of IPs in subnet):
S
S
S
H
H
H
H
H
 | Range | Binary | host IP range
Net ID Broadcast | 0 – 31 32-63 64-95 96-127 128-159 160-191 192-223 224-255 |  | 

## Slide 42: Subnet
Ex: Subnet for class C
/25
/26
/27
/28
/29
/30
/31
/32
How about 0 bits borrowed?

## Slide 43: Subnet
All-zero subnet: network address of “parent” before subnetting
All-one subnet: broadcast of “parent”
 Not to use 2 above-mentioned subnets to avoid confusion.
 No. of Subnets = 2n - 2
However, some of latest network devices can support to work for these subnets

## Slide 44: Classless Inter-Domain Routing (CIDR)
Classless Inter-Domain Routing (CIDR)
  Limitation of IP class
    Class A –16+ million hosts
    Class B – 65,535 hosts
    Class C – 254 hosts
Subnet Address Extensions

## Slide 45: Public/Private IP
Private IP

## Slide 46: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 47: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 48: Exercise
A company has 3 departments with 30 PCs (total),
Each department requires a private LAN (subnet) with 10PCs
Design a LAN and assign IP addresses to this LAN
  What IP class we need to apply? Class C: 192.168.1.xx / 255.255.255.0
  3 subnets (3 departments) => 192.168.1.xx/255.255.255.192

## Slide 49: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 50: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 51: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 52: DHCP: more than IP addresses
DHCP can return more information than just allocated IP address on subnet:
  address of first-hop router for client (default gateway)
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 53: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 54: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

## Slide 55: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 56: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 57: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:

## Slide 58: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 59: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 60
5.1 Overview of Network layer
  data plane
  control plane
5.2 What’s inside a router
5.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
  NAT
5.4 routing protocols
link state
distance vector
5.5 intra-AS routing in the Internet: OSPF
5.6 routing among the ISPs: BGP
5.7 The SDN control plane
5.8 ICMP: The Internet Control Message Protocol
5.9 Network management and SNMP
Chapter 5: outline
Data Plane
Control Plane

## Slide 61: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 62: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 63: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 64: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 65: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  address shortage should be solved by IPv6
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?

## Slide 66
5.1 Overview of Network layer
  data plane
  control plane
5.2 What’s inside a router
5.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
5.4 routing protocols
link state
distance vector
5.5 intra-AS routing in the Internet: OSPF
5.6 routing among the ISPs: BGP
5.7 The SDN control plane
5.8 ICMP: The Internet Control Message Protocol
5.9 Network management and SNMP
Chapter 5: outline
Data Plane
Control Plane

## Slide 67: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 68: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 69: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 70: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 71: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 72: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4

## Slide 73: IPv6: adoption
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
  Why?

## Slide 74
5.1 Overview of Network layer
  data plane
  control plane
5.2 What’s inside a router
5.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
  Generalized Forward and SDN
5.4 routing protocols
link state
distance vector
5.5 intra-AS routing in the Internet: OSPF
5.6 routing among the ISPs: BGP
5.7 The SDN control plane
5.8 ICMP: The Internet Control Message Protocol
5.9 Network management and SNMP
Chapter 4: outline
Data Plane
Control Plane

## Slide 75
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 76
Generalized Forwarding and SDN
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each router contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions

## Slide 77: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Flow table in a router (computed and distributed by controller) define router’s match+action rules

## Slide 78: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard

## Slide 79: OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Notes: Now I’ll describe the API that tries to meet these goals.
79

## Slide 80
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
Examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1

## Slide 81
Destination-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port3
Examples
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 6
22:A7:23:
11:E1:02

## Slide 82: OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies different kinds of devices

## Slide 83: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 84
Chapter 5: Summary!
Question: how do forwarding tables (destination-based forwarding) or flow tables (generalized forwarding) computed?
Answer: by the control plane (next section)
4.1 Overview of Network layer: data plane and control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  NAT
  IPv6
4.4 Generalized Forward and SDN
  match plus action
  OpenFlow example